## Slide 1: Project Overview
Objective: Examine the influence of congestion pricing on peak-hour travel from NJ to NYC.
Approach: Use multinomial logit and mixed logit models for behavior analysis.
Impact: Provide insights into policy design and urban traffic management strategies.

## Slide 2: Survey Design
Demographics
Psychological
Mode choice at different
  congestion fee
  Travel time
  Travel time difference
We got 153 respondents in Hudson, NJ

## Slide 3: Survey Data Description

## Slide 4: Methodology
Pooled Model
  Multinomial Logit Model (MNL)
  Mixed Logit Model (MXL)
Segmentation test for Commuters' Belief in Congestion fee Effectiveness (MNL & MXL)
  Confident in Effectiveness
  Skeptical in Effectiveness

## Slide 5: Model
MXL
𝑈i𝑛t = 𝜷int x𝑖𝑛t + 𝜀int , where 𝜀𝑖nt i.i.d Gumbel , 𝜷int~ f(𝜷|θ).
Model heterogeneity
Iterate over all Individual Specific Attribute Combinations:
All coefficient p value < 0.1, Maximize McFadden's R Square
Mode Choice ~ Time + Cost |1+Income+CommuteMode| 0
Attributes
Alternative Specific: Travel Time, Travel Cost
Individual Specific: Age, Gender, Occupation(dummy), Income, Current commute mode
MNL
𝑈𝑖𝑛 = 𝜷𝑖 x𝑖𝑛 + 𝜀𝑖n , where 𝜀𝑖n i.i.d Gumbel.
Indifferent taste among population

## Slide 6: Pooled Model Result
Table 1. Pooled model result
Variable | Pooled | 
 | MNL | MXL
Intercept: Auto | 0.642 | 0.272
Annual Household Income ($):Auto | 0.098* | 0.208*
Usual Commute Mode: Auto | -1.936*** | -3.855***
Travel Time | 0.043*** | 0.150***
Travel Cost | -0.087*** | -0.316***
sd.Time |  | 0.163***
sd.Cost |  | 0.129***
Log-Likelihood | -463.23 | -343.97
McFadden R^2 (LL_C) | 0.18404 | 0.39412
McFadden R^2 (LL_0) | 0.213 | 0.415
Higher Household Income
→ Automobile
Tend to maintain commute mode
Longer Travel Time
→ Automobile
Larger Travel Cost
→ Public Transit
MXL: Better fit. Significant individual heterogeneity
For MXL,
βTime ∼N(0.15,0.0266), βCost ∼ N(-0.316,0.0166)

## Slide 7: Segmentation Test Result
Table 2. Segmentation test result
Likelihood Ratio Test:
Test Statistic = 182.1157
Dof = 7
P value < 0.01
→ Reasonable Segmentation
Skeptical group:
  Income not significant
  more sensitive to change in travel time and cost
Slightly better fit than pooled model
Variable | More Belief in Effectiveness |  | Less Belief in Effectiveness | 
 | MNL | MXL | MNL | MXL
Intercept: CAR | 2.074** | 3.070** | 0.612 | 4.719**
Annual Household Income ($):CAR | 0.261** | 0.577** |  | 
Usual Commute Mode: CAR | -2.056*** | -3.499*** | -1.976*** | -5.318***
Travel Time | 0.049*** | 0.133*** | 0.067*** | 0.273***
Travel Cost | -0.054* | -0.172** | -0.143*** | -0.437***
sd.Time |  | 0.131*** |  | 0.191***
sd.Cost |  | 0.095** |  | 0.124**
Log-Likelihood | -167.06 | -130.45 | -171.23 | -122.46
McFadden R^2 (LL_C) | 0.19552 | 0.37183 | 0.25135 | 0.46456
McFadden R^2 (LL_0) | 0.716 | 0.778 | 0.709 | 0.792

## Slide 8: Sensitivity of Cost
Elasticity of probability of choosing Automobile to Automobile Travel Cost for :
ePn(Auto),xAuto,Cost,n = βAuto,CostxAuto,Cost,n(1-Pn(Auto))
Confident in Effectiveness Group: Elasticity = -2.25.
  Congestion fee increasing 1% → loosing 2.25% probability of choosing Auto
Skeptical in Effectiveness Group: Elasticity = -5.11.
  Congestion fee increasing 1% → loosing 5.11% probability of choosing Auto
  More sensitive to cost change

## Slide 9: Next Steps
Predict the drop in NJ-NY commuting automobile trips under different congestion pricing schemes

## Slide 10: Reference
[1] Regional Plan Association (RPA). (n.d.). Congestion Pricing in NYC. Accessed February 9, 2024, from https://rpa.org/work/reports/congestion-pricing-in-nyc
[2] HNTB. (n.d.). Fix NYC Report. Accessed February 9, 2024, from https://www.hntb.com/fix-nyc-report/
[3] He, B. Y., Zhou, J., Ma, Z., Chow, J. Y. J., & Ozbay, K. (2020). Evaluation of city-scale built environment policies in New York City with an emerging-mobility-accessible synthetic population. Transportation Research Part A: Policy and Practice, 141, 444-467. https://doi.org/10.1016/j.tra.2020.10.006
[4] (2021). A validated multi-agent simulation test bed to evaluate congestion pricing policies on population segments by time-of-day in New York City. Transport Policy, 101, 145-161. https://doi.org/10.1016/j.tranpol.2020.12.011
[5] Cai, Y., Ong, G. P., & Meng, Q. (2023). Understanding bike-sharing as a commute mode in Singapore: An agent-based simulation approach. Transportation Research Part D: Transport and Environment, 122, 103859. https://doi.org/10.1016/j.trd.2023.103859
[6] Cipriani, E., Mannini, L., Montemarani, B., Nigro, M., & Petrelli, M. (2019). Congestion pricing policies: Design and assessment for the city of Rome, Italy. Transport Policy, 80, 127-135. https://doi.org/10.1016/j.tranpol.2018.10.004